## Slide 1: ToMaTo
A network experimentation tool
Dennis Schwerdel

## Slide 2: Overview
Introduction
ToMaTo
  Architecture
  Devices
  Connectors
  Features
  Editor
Evaluation
Integration in German-Lab

## Slide 3: Introduction
Why experimental facilities?
  Helps designing, testing and improving network algorithms, applications and arcghitectures
  Instrument for networking research
Existing experimental facilities
  Planet-Lab
    High node numbers → allows large experiments
    Uses container virtualization → limited hardware and kernel access
    Shared network interfaces → no network topologies
  Emulab
    No virtualization → full hardware and kernel access, inefficient
    Realized as cluster → full control over network topology
  Seattle
    Only custom python dialect → not suitable for all experiments

## Slide 4
Architecture
Devices
Connectors
Features
Graphical editor
ToMaTo

## Slide 5: ToMaTo
ToMaTo: „Topology Managenemt Tool“
Topology contains
  Devices
  Connectors
Devices
  Active components
  E.g. computers
  Produce/Consume data
Connectors
  Networking components
  E.g. switches, routers
  Transport/Manipulate data

## Slide 6: ToMaTo - Architecture
ToMaTo contains 3 parts
Host part
  Based on PROXMOX VE
  Offers virtualization
  All additional software available as packages
Backend
  Controls hosts via SSH
  Centralized logic, resource management, user accounts
  Offers XML RPC interface
Frontend(s)
  Offer a GUI to users
  Currently only a web-based interface exists
  More frontends possible

## Slide 7: ToMaTo - Devices
KVM
  Full virtualization
  Offers full access
OpenVZ
  Container virtualization
  Lightweight, uses less resources
  Easier to access
Templates
  Preinstalled device images, ready to use
  Current versions of Debian and Ubuntu Linux (32 and 64 bits)
  FreeBSD (only KVM)

## Slide 8: ToMaTo - Connectors
Tinc VPN
  Creates private networks between devices
  Not encrypted → good performance
  Hub, Switch or Router semantics
Special connectors
  Connect devices to host bridges
  Can connect devices to the Internet
  Openflow integration planned
Link emulation
  Only available for Tinc VPN
  Can set additional QoS limitations on links
    Packet loss
    Bandwidth limit
    Latency
  Long-term statistics help users to estimate underlying link properties

## Slide 9: ToMaTo - Features
Administrator/Developer features
  Intelligent load-balancing
  Open xml-rpc interface
  Administrator tools
  LDAP integration
User features
  Automatic network interface configuration
  Changes to running topologies
  Console access
  Image up/download
  Pcap capturing

## Slide 10: ToMaTo – Graphical editor (1)

## Slide 11: ToMaTo – Graphical editor (2)
Topology Creator
Automatically creates topologies
  Ring topology
  Star topology
  Full mesh
Connects topologies
Configures network interfaces
  IP addresses
  Netmasks

## Slide 12
Methodology
Access layer experiments
Network layer experiments
Algorithm/Protocol experiments
Legacy software experiments
Evaluation

## Slide 13: Evaluation (1)
Methodology
  Identify network experiment classes
  Evaluate ToMaTo support for these classes
Access layer experiments
  Consider lower layers and hardware
    Example: Mobile handover
  Requirements
    Hardware access
    Custom operating systems (Realtime)
    Heterogeneous access technologies (3G, Wifi, etc.)
    Complex setup, depending on hardware type
  Needs specialized testbeds depending on hardware
    DES Testbed, Wisebed

## Slide 14: Evaluation (2)
Network layer experiments
  Focus on TCP/IP suite
    Example: IPv6 extensions, TCP substitutes
  Requirements
    Deep OS access (modified kernels, etc.)
    Small but complex topologies, link emulation
  ToMaTo offers
    Full kernel access via KVM
    Complex topologies
    Link emulation
    Packet capturing (for analysis)
    Easy setup of topologies

## Slide 15: Evaluation (3)
Algorithm/Protocol experiments
  Work on top of network layer
    Example: P2P-Networks
  Requirements
    Huge but simple topologies
    Link emulation
    No hardware or OS access
  ToMaTo offers
    Lightweight virtualization with OpenVZ (250 devices per host)
    Link emulation
    Ability to connect to other testbeds via Internet
    Up/download of images (simplifies setup of multiple devices)

## Slide 16: Evaluation (4)
Legacy software experiments
  Considers legacy software
    „Legacy software“ refers to any widespread software with undocumented or unpublished behavior
    Example: Skype and Windows
  Requirements
    Special environments, custom operating systems
    Access to external services
    Small but complex topologies
    Link emulation and external packet capturing
  ToMaTo offers
    Custom operating systems with KVM (even Windows and BSD run)
    Acces to external service via Internet connector
    Packet capturing independent of guest OS

## Slide 17
ToMaTo summary
German-Lab integration
Summary

## Slide 18: ToMaTo Summary
Flexible and extensible
  3-tier architecture
  Openflow integration being developed
Efficient
  As much access as needed (KVM)
  As less resource usage as possible (OpenVZ)
Easy to use
  Graphical editor, topology creator
  Automatic interface configuration
Supports experiments
  Ready-to-use templates
  Link emulation
  Image download/upload
  Packet capturing
  Direct console access

## Slide 19: German-Lab Integration
Embedded in SIG Facility
  But not bound to German-Lab
20 German-Lab hosts already ToMaTo-enabled
  Access via http://tomato.german-lab.de
Direct account integration via LDAP
  All German-Lab users can access ToMaTo
Joint development
  Host part, Backend, Frontend
    University of Kaiserslautern (Dennis Schwerdel)
  Topology creator (part of graphical editor)
    University of Würzburg (David Hock)
  Openflow integration (current development)
    University of Würzburg (Student work)

## Slide 20
Dipl.-Inf. Dennis Schwerdel
Phone: +49 (0)631 205-26 43
Fax: +49 (0)631 205-30 56
Email: schwerdel@informatik.uni-kl.de
Internet: http://www.icsy.de